## Slide 1: Science Visualization
Vector Visualization Techniques

## Slide 2: Introduction
What’s Vector Field Visualization?
  A sub-branch of scientific visualization
  Depiction of magnitude + direction (as opposed to scalar field visualization)
  Various applications in our daily life: automotive simulation, aerodynamics, turbo machinery, meteorology, oceanography, medical visualization
Visualization of flow around a car [source: Garth, 2008]
Arrows showing the wind
direction and magnitude [source: Turk, 1996]

## Slide 3: Vector Visualization
Data set is given by a vector component and its magnitude often results from study of fluid flow or by looking at derivatives (rate of change) of some quantity trying to find out what to see and how!
Many visualization techniques proposed
  Hedgehogs/glyphs
  Particle tracing
  stream-, streak-, time- & path-lines
  stream-ribbon, stream-surfaces, stream-polygons, stream-tube
  hyper-streamlines
  Line Integral Convolution

## Slide 4: Vector Visualization - Origin
Where are those methods coming from??
  Rich field of Fluid Flow Visualization
  Modern domain - Computational Field Simulations
Vector visualization
  Gaseous flow:
    development of cars, aircraft, spacecraft
    design of machines - turbines, combustion engines
  Liquid Flow:
    naval applications - ship design
    civil engineering - harbor design, coastal protection
  Chemistry - fluid flow in reactor tanks
  Medicine - blood vessels, SPECT, fMRI

## Slide 5: Flow Visualization
What is the problem definition?
  Given (typically):
    physical position (vector)
    pressure (scalar),
    density (scalar),
    velocity (vector),
    entropy (scalar)
  steady flow - vector field stays constant
  unsteady - vector field changes with time
The goal
  What are we looking for?
  Answer: ANY UNDERSTANDING!

## Slide 6: Flow Visualization - traditionally
Traditionally
  Experimental Flow Visualizations
How?
  Three basic techniques:
    adding foreign material
    optical techniques
    adding heat and energy
Problems:
  the flow is affected by experimental technique
  not all phenomena can be visualized
  expensive (wind tunnels, small scale models)
  time consuming

## Slide 7: Dimensions
Spatial dimension:
  2D (planar flow)
  2.5D (boundary flow, flow on surface)
  3D (real-world flow, volumetric flow)
Temporal dimension:
  Steady flow: one time step (or instantaneous or static flow)
  Time-dependent flow: multiple time steps (or unsteady or transient, real-world)

## Slide 8: Overview
Vector fields (VFs) typically used to encode many different data sets:
  e.g. Velocity/Flow, E&M, Temp., Stress/Strain
Area of interest: Visualization of VFs
Problem: Data overload!
  One solution: Visualize a “skeleton” of the VF by viewing its topology

## Slide 9: Vector Fields
A steady vector field (VF) is defined as a mapping:
  v: N → TN, N a manfold, TN the tang. bundle of N
    In general, N = TN ≈ Rn
An integral curve is defined by a diff. eqn:
  df/dt = v(f(t)), with fo, to as initial conditions
  Also called streamlines

## Slide 10: Vector Fields
A phase portrait is a depiction of these integral curves:
Image: A Combinatorial Introduction to Topology, Michael Henle

## Slide 11: Critical Points
A critical point is a singularity in the field such that v(x) = 0.
Critical points are classified by eigenvalues of the Jacobian matrix, J, of the VF at their position:
  e.g. in 2d,
If J has full rank, the critical point is called linear or first-order
Hyperbolic critical points have nonzero real parts

## Slide 12: Critical Points
Image: Surface representations of 2- and 3-dimensional fluid flow topology, Helman & Hesselink

## Slide 13: Critical Points
Generally:
  R > 0 refers to repulsion
  R < 0 refers to attraction
    e.g. a saddle both repels and attracts
  I ≠ 0 refers to rotation
    e.g. a focus and a center
  Note in 2d case I1 = -I2

## Slide 14: Sectors & Separatrices
In the vicinity of a critical point, there are various sectors or regions of different flow type:
  hyperbolic: paths do not ever reach c.p.
  parabolic: one end of all paths is at c.p.
  elliptic: all paths begin & end at c.p.
A separatrix is the bounding curve (or surface) which separates these regions

## Slide 15: Sectors & Separatrices
Images: A topology simplification method for 2D vector fields. Xavier Tricoche, Gerik Scheuermann, & Hans Hagen

## Slide 16: Sectors & Separatrices
Images: A topology simplification method for 2D vector fields. Xavier Tricoche, Gerik Scheuermann, & Hans Hagen

## Slide 17: Vector Field Visualization
A vector field:
F(U) = V
  U: field domain
    (x,y) in 2D
    (x,y,z) in 3D
  V: vector (u,v) or (u,v,w)
Like scalar fields, vectors are defined at discrete points

## Slide 18: Classification
Direct
  Overview of vector field, minimal computation, e.g. glyphs, colour mapping
Feature-based
  Provides suggestive visualization by extracting subsets of data before visualization, e.g. vector field clustering
Texture-based
  Covers domain with a convolved texture, e.g., Spot Noise, LIC, ISA, IBFV(S)
Geometric
  Coherent representation, integration-based geometric techniques, e.g. streamlines

## Slide 19: Vector Field Visualization Applications
Vector field clustering
Hedgehog

## Slide 20: Vector Field Visualization Applications
Computational Fluid Dynamics
Weather modeling

## Slide 21: Applications of Vector Field Visualization
The major application area is Computational Fluid Dynamics where we wish to visualize the velocity field within a volume, or on a surface
... but has applications to any other discipline where flow is involved
  for example, the flow of population in social sciences
Important distinction between steady and unsteady (time-dependent) flow

## Slide 22: Applications of Vector Field Visualization
Experimental fluid dynamics:
  aim to get impression of flow around a scale model of object (eg smoke in wind tunnel)
  disadvantages in cost, time and integrity
Computational fluid dynamics
  simulation of the flow (Navier-Stokes equations)
  visualization of the resulting velocity field so as to mimic the experimental techniques

## Slide 23: Applications of Vector Field Visualization
Techniques
  Time lines
    row of small particles (hydrogen bubbles) released at right angles to flow - motion of ‘line’ shows the fluid flow
  Streak line
    dye injected from fixed position for period of time - tracer of dye shows the fluid flow
  Path line
    small particles (magnesium powder in liquid; oil drops in gas) - velocity measured by photographing motion with known exposure time
  Visualization of flow field on surface of object achieved by fixing tufts at several points on surface - orientation of threads indicates direction of flow
Notes:   Notice distinction:
    tufts show flow past a fixed point (Eulerian)
    bubbles etc show the flow from point of view of a floating object (Lagrangian)

## Slide 24: Vector Field Visualization Challenges
General Goal
  Display the field’s directional information
Domain Specific:
  Detect certain features, Vortex cores, Swirl

## Slide 25: Vector Field Visualization Challenges
A good vector field visualization is difficult to get:
  Displaying a vector requires more visual attributes
  (u,v,w): direction and magnitude
  Displaying a vector requires more screen space
    more than one pixel is required to display an arrow
    ==> It becomes more challenging to display a dense vector field

## Slide 26: Vector Field Visualization Challenges
Local technique:
  Particle Advection: Display the trajectory of a particle starting from a particular location
Global technique:
  Display the flow direction everywhere in the field
  Hedgehogs, Line Integral Convolution, Texture Splats etc.

## Slide 27: Computer Flow Visualization
Now look at methods for computer aided flow visualization
Assume initially velocity field given on 3D Cartesian grid
velocity
vx, vy, vz
given at each
grid point
hexahedral
cells

## Slide 28: Using Scalar Techniques
Sometimes it is useful to derive scalar quantities from the velocity field
For example, velocity magnitude
  speed = sqrt (vx2 + vy2 + vz2)
How would these be visualized?

## Slide 29: Arrows
Very simple technique
Arrow drawn at each grid point showing direction and size of velocity
This works effectively
enough in 2D

## Slide 30: Arrows
But in 3D it suffers from perception problems:
Of course the picture quickly gets cluttered too

## Slide 31: Arrows
Arrows can be used successfully in 3D as follows:
  by slicing the volume, and attaching arrows (with shadow effects) to the slice plane - this gives a hedgehog effect
  by giving more spatial cues - drawing arrows as true 3D objects
but clutter again a
problem!
{BTW - Eulerian or Lagrangian?}

## Slide 32: Local technique - Particle Tracing
Visualizing the flow directions by releasing particles and calculating a series of particle positions based on the vector field
The motion of particle: dx/dt = v(x)
  x: particle position (x,y,z)
  v(x): the vector (velocity) field
Use numerical integration to compute a new particle position
  x(t+dt) = x(t) + Integration( v(x(t)) dt )

## Slide 33: Tufts

## Slide 34: Particle Traces
This is analogous to experimental path lines - we imagine following the path of a weightless particle
Suppose initial position (seed point) is
(x0, y0, z0)
The aim is to find how the path develops over time
( x(t), y(t), z(t) )
Also called particle advection

## Slide 35: Particle Traces
Motion of a particle is given by:
dx/dt = vx; dy/dt = vy; dz/dt = vz
  Three ordinary differential equations with initial conditions at time zero:
  x(0) = x0; y(0) = y0; z(0) = z0
In 2D, we have:
(x0,y0)
(vx,vy) is
rate of change
of position

## Slide 36: Particle Tracing
Numerical Techniques for Integrating the ODEs
  Simplest technique is Euler’s method:
  dx/dt = ( x(t+t) - x(t)) / t = vx(p(t)), p=(x,y,z)
  hence
  x(t+t) = x(t) + t.vx(p(t))
  Similarly, for y(t) and z(t)
In 2D, we have:
(x0,y0)
(x1,y1)
(t.vx,t.vy)

## Slide 37: Path Tracing
Interpolation
  As the solution proceeds, we need velocity values at interior points
  (vx, vy, vz) is calculated at current point (x,y,z) - by trilinear interpolation for example.
In 2D, we have:
(x0,y0)
(x1,y1)
(vx,vy) found
by interpolation
(bilinear)

## Slide 38: Particle Tracing
Point Location
  When we leave one cell, we need to determine which cell the new point belongs to
(x0,y0)
(x1,y1)
- this is quite straightforward for Cartesian grids

## Slide 39: Particle Tracing - Algorithm
Algorithm
find cell containing initial position
{point location}
While particle in grid
determine velocity at current position
{interpolation}
calculate new position
{integration}
find cell containing new position
{point location}
Endwhile

## Slide 40: Numerical Integration
First Order Euler method:
x(t+dt) = x(t) + v(x(t)) * dt
  Not very accurate, but fast
  Other higher order methods are available:
    Runge-Kutta second and fourth order integration methods (more popular due to their accuracy)
Result of first order Euler method

## Slide 41: Numerical Integration
Second Runge-Kutta Method
  x(t+dt) = x(t) + 0.5 * (K1 + K2)
  k1 = dt * v(x(t))
  k2 = dt * v(x(t)+k1)
  Standard Method: Runge-Kutta fourth order
  x(t+dt) = x(t) + 1/6 *(k1 + 2*k2 + 2*k3 + k4)
  k1 = dt * v(t); k2 = dt * v(x(t) + k1/2)
  k3 = dt * v(x(t) + k2/2); k4 = dt * v(x(t) + k3)
0.5 * [v(x(t))+v(x(t)+dt*v(x(t))]
x(t+dt)
x(t)

## Slide 42: Stream Lines
Mathematically, stream lines are lines everywhere tangential to the flow
For a steady flow
  What is the relation between stream lines and particle traces?
  A curves that connect all the particle positions
stream lines

## Slide 43: Streamlines
Displaying streamlines is a local technique because you can only visualize the flow directions initiated from one or a few particles
When the number of streamlines is increased, the scene becomes cluttered
You need to know where to drop the particle seeds
Streamline computation is expensive

## Slide 44: Rendering Streamlines
In 3D, curves are hard to understand without depth cues
Ideas used include:
  stream ribbons - each streamline drawn as a thin flat ribbon, showing twist; or two adjacent streamlines connected into ribbon, showing twist and divergence
  tubes

## Slide 45: Unsteady Flow Visualization
Recent research interest has been in the more complex case of unsteady flows, where velocity depends on time
Particle traces, streak lines and time lines can all be used
Streak lines seem to give the best results

## Slide 46: Flow Visualization - Texture Effects
A new class of image-based methods attempts to visualize flow as a texturing effect
Most successful for 2D flow - and also for flow over surfaces in 3D
Methods include:
  spot noise
  line integral convolution - lic

## Slide 47: Pathlines, Timelines, and Streaklines
Extension of streamlines for time-varying data
  Pathlines:
  Timelines:
    Release a line of particles at same instant and draw a curve through the positions at successive time intervals
T=1
T=2
T=3
T=4
T=5
T = 1
T = 2
T = 3
timeline

## Slide 48: Streaklines
Continuously injecting a new particle at each time step, moving all the existing particles and connect them together into a streakline.
  release continuous flow of particles for a short period
b.t. =5
b.t. =4
b.t. =3
b.t. =2
b.t. =1

## Slide 49: Global techniques
Display the entire flow field in a single picture
  Minimum user intervention
  Example: Hedgehogs (global arrow plots)

## Slide 50: Hedgehogs
Dense 2D fields or 3D fields are difficult

## Slide 51: Vector Field Clustering
Simplified Representation of Vector Fields
  Dimensions: 3D, Steady
  Concept:
    a hierarchical clustering based method which presents a suggestive overview of vector fields
  Implementation:
    Bottom-up fashion
    Merger driven by similarity error metric
    Interaction

## Slide 52: Comparison: Scalar vs. Vector visualization
Scalar data in 3D: As points

## Slide 53: Comparison: Scalar vs. Vector visualization
Scalar data in 3D: Cutplanes

## Slide 54: Comparison: Scalar vs. Vector visualization
Scalar data in 3D: Regions of interest

## Slide 55: Comparison: Scalar vs. Vector visualization
Scalar data in 3D: Iso-surfaces

## Slide 56: Comparison: Scalar vs. Vector visualization
Scalar data in 3D: Volume visualization

## Slide 57: Comparison: Scalar vs. Vector visualization
Vector data in 3D: Vector glyphs

## Slide 58: Comparison: Scalar vs. Vector visualization
Vector field: Streaklines

## Slide 59: Comparison: Scalar vs. Vector visualization
Vector field: Ribbons

## Slide 60: Technique: Vector field ribbons
Notes: 60

## Slide 61: Texture-based Visualization
A new class of image-based methods attempts to visualize flow as a texturing effect
  Dimensions: 2.5D, Unsteady
  Concept
    Dense and coherent representations for unsteady flow on surfaces
  Implementation:
    Most successful for 2D flow - and also for flow over surfaces in 3D
    Project vector field to image space
    Advection mesh is distorted according to pathlines
    Texture is distorted and attached based on the distorted mesh
    Blend noise in image space
Methods include:
  Spot noise
  Line integral convolution (LIC)

## Slide 62: Spot Noise for Flow Visualization
Spots of random size and intensity drawn in a plane give a texture effect
Texture defined as an intensity function f:
f( x ) = ∑ ai h( x - xi )
where xi is random position, ai is random scale (zero mean), and h is the spot function - zero everywhere except for small area (here circular)
one spot
many spots
spot texture

## Slide 63: Spot Noise for Flow Visualization
Different textures result from different spot shapes
Aligning the shape of the spot with the direction of flow gives a good visualization effect
In direction of flow, scale proportional to ( 1 + |v | ) , |v| = velocity magnitude
At 90°to flow, scale proportional to 1 / (1 + |v|)

## Slide 64: Spot Noise Example

## Slide 65: Flow Over a Surface
Wall friction displayed
using oil and paint - wind
evaporates oil and paint
leaves white traces
Numerical simulation
of flow, visualized
using spot noise

## Slide 66: Spot Noise Example

## Slide 67: Spot Noise Movie

## Slide 68: Line Integral Convolution (LIC)
It is a technique proposed by Brian Cabral and Leith Leedom to visualize fluid motion.
  Compared with simpler integration-like techniques, where one follows the flow vector at each point to produce a line, it has the advantage of producing a whole image at every step.
How ?
  Intuitively, the flow of a vector field is visualized by adding a random static pattern of dark and light paint sources.
  As the flow passes by the sources each parcel of fluid picks up some of the source color, averaging it with the color it has already acquired.
  The result is a random striped texture where points along the same streamline tend to have similar color.

## Slide 69: Line Integral Convolution (LIC)
Essence of method is:
  Consider a white noise texture, T(x,y)
  for each pixel, set its intensity as a function (e.g. average) of values of T along a short streamline segment through the pixel
  This has effect of correlating the resulting pixel values along streamlines, so a sense of the flow direction is obtained.

## Slide 70: LIC Example

## Slide 71: LIC Example
Flow over surface of car - from CIRA, Italy
Italian Aerospace Research Centre

## Slide 72: LIC Example
Flow underneath car - from CIRA, Italy

## Slide 73: LIC Developments - Oriented LIC
Original LIC shows direction of flow but not orientation (i.e. -> or <- )
Oriented LIC uses a sparse texture and a weighting of samples along streamline to give orientation effect

## Slide 74: Comparison (LIC and Streamlines)

## Slide 75: LIC on 3D surfaces and volumes

## Slide 76: Texture Splats

## Slide 77: Spot Noise

## Slide 78: Line bundles

## Slide 79: Vector Field Topology
This approach aims to visualize only the significant features of a flow field
It identifies critical points
  points where velocity magnitude is zero
  point of repulsion, attraction or a saddle point
  streamlines from critical points divide space into regions of similar behaviour

## Slide 80: Planar Topology
Planar topology of a VF is simply a graph with the critical points as nodes and the separatrices as edges. e.g.:

## Slide 81: Poincaré Index
Another topological invariant
The index (a.k.a. winding number) of a critical point is number of VF revolutions along a closed curve around that critical point
By continuity, always an integer
The index of a closed curve around multiple critical points will be the sum of the indices of the critical points

## Slide 82: Poincaré Index
The index around no critical point will always be zero
For first order critical points, saddle will be -1 and all others will be +1
There is a combinatorial theory that shows:

## Slide 83: Three Dimensions
In 3D, we classify critical points in a similar manner using the 3 eigenvalues of the Jacobian
Broadly, there are 2 cases:
  Three real eigenvalues
  Two complex conjugates & one real

## Slide 84: Three Dimensions
Images: Saddle Connectors – An approach to visualizing the topological skeleton of complex 3D vector fields, Theisel, Weinkauf, Hege, and Seidel
Left-to-right: Nodes, Node-Saddles, Focus, Focus-Saddles
Top: Repelling variants; Bottom: Attracting variables
Left-half: 3 real eigenvalues; Right-half: 2 complex eigenvalues

## Slide 85
Separatrices now become 2d surfaces and 1d curves.
Thus topology of first-order critical points will be composed of the critical points themselves + curves + surfaces
Images: Saddle Connectors – An approach to visualizing the topological skeleton of complex 3D vector fields, Theisel, Weinkauf, Hege, and Seidel
Three Dimensions

## Slide 86: Attachment and Detachment Points
There are also critical points along surfaces, where streamlines start (detachment points) or end (attachment points)
The flow field topology is produced by:
  identifying critical points
  drawing streamlines from detachment or attachment points and saddles (4 from saddles)... to repulsors and attractors
  drawing streamlines to/from critical points that exit boundary

## Slide 87: Flow Topology on Surface

## Slide 89
Questions ?