## Slide 1: Control, Monitoring, Diagnosis, and Planning
Lecture 12

## Slide 2: Fuzzy Control
Fuzzy control systems were one of the first industrial fuzzy systems. The first system was designed and implemented by Mamdany for cement kiln control in the United Kingdom in the early 1970s.
Since then many fuzzy control systems have been developed, for example, subway control, washing machines, camera focusing, automatic transmission control, rice cookers, dishwashers, and many other engineering applications. Intelligent robotics is an area where fuzzy control systems will be used in the future.

## Slide 3: Fuzzy Control
By fuzzy control, an application of fuzzy logic to control problems is meant. Fuzzy control is different from standard control, mainly in three respects:
the use of linguistically described concepts, rather than formulas;
the use of commonsense knowledge, rather than mathematical knowledge; and
The use of methods of fuzzy logic.

## Slide 4: Fuzzy Control
Ordinary controllers usually represent a system's uncertainty by a probability distribution. Probability models describe the system's behavior with the use of first-order and second-order statistics—means and covariance. Mathematical models of control systems facilitate a mean-square-error (MSE) analysis of the system's behavior.

## Slide 5: Fuzzy Control
In case of many variables, it is extremely difficult to accurately articulate such mathematical models. They also require a lot of computations, which might be difficult to perform in real time. Fuzzy control systems consist of fuzzy rules and an inference machine which includes fuzzification and defuzzification. The system works in a cycle, as shown graphically in figure on next slide.

## Slide 6: Fuzzy Control
A block diagram of a fuzzy control system.

## Slide 7: Fuzzy Control
The case example of the Inverted Pendulum Problem is discussed below. After fuzzy quantization of the two input parameters angle Θ and angular velocity ΔΘ, and the output parameter, the force applied to the cart, by using seven fuzzy labels, seven rules were set experimentally by Professor Yamakawa (1989). They are shown in the form of a rule map in figure on next slide along with the membership functions of the fuzzy labels.

## Slide 8: Fuzzy Control
A set of fuzzy rules and membership functions for the Inverted Pendulum case problem.

## Slide 9: Fuzzy Control
By using the same approach, much more complex tasks can be solved.
For complex control tasks, a modular system, which comprises two or more simple control systems, can be designed as demonstrated in an example solved in next lecture.
In the fuzzy control systems the control algorithm is described by fuzzy words and not analytically.

## Slide 10: Fuzzy Control
Therefore it is difficult to evaluate the stability of the model, that is, how stable the system will be if some parameters of the objects change, for example, the length of the pendulum, the weight of the mouse put on top of a pendulum, and so forth.
This problem has been thoroughly investigated by Li-Xin Wang (1994).
In adaptive fuzzy control systems the set of fuzzy rules dynamically change according to the changes in the process or object under control (see Brown and Harris 1994, Wang 1994).

## Slide 11: Monitoring
Fuzzy theory is useful for creating monitoring systems when the parameters and the conditions to be monitored can be expressed in fuzzy linguistic terms.
Using fuzzy rules makes the system more sensitive to the borderline values for the parameters.
Monitoring of a process that is described by a large number of parameters can be handled in a similar way.

## Slide 12: Diagnosis
Diagnosis is a generic problem suitable for solving by the methods of fuzzy logic. This is because of ambiguity in the diagnostic process. The latter may have many causes; for example, the earlier we try to diagnose an abnormality, the more ambiguous the indicators are; the difference between the normal and abnormal state might be slight.

## Slide 13: Diagnosis
Fuzzy diagnostic systems can contain fuzzy rules of two different forms:
IF disorders (x), THEN symptoms (y); in this case x is sought from the set of equations: y = x ¤ R, where R is the set of relations between the disorders and the symptoms and "¤" denotes a composition operator; this is the inverse problem of the fuzzy inference composition rule and more difficult to solve.
IF symptoms (x), THEN disorders (y); in this case y is sought from the fuzzy compositional equation y = x ¤ R

## Slide 14: Diagnosis
More sophisticated fuzzy diagnostic systems use fuzzy concepts for representing not only static symptoms but their dynamic properties too, for example, "tendency"—"increasing," "decreasing,'' "not changing," etc.
In some fuzzy medical diagnostic systems patients are allowed to answer in fuzzy terms, for example, the question "Do you feel fatigue?" could be answered by using the fuzzy concepts "seldom,“ "sometimes," "always.'' There answers can be processed further as fuzzy input values.

## Slide 15: Planning
Planning in uncertain and ambiguous conditions is also a problem, too difficult to be tackled by the traditional symbolic AI methods.
Take the Monkey and Bananas case example. When the exact positioning of all the objects and exact goals are known, there is no problem.
But suppose we do not have the exact positioning of the monkey and instead of the exact position, for example (5,8), we know that the monkey is "near" the couch, the ladder is "at about the most distant corner from the monkey,“ and bananas are on the ceiling "somewhere in the middle."

## Slide 16: Planning
The goal can be "monkey to grasp bananas."
A plan in this case can be generated by using a set of fuzzy rules and a fuzzy inference machine to perform the reasoning process.
Complex planning problems can be solved in stages, for example, first stage, recognition of the situation; second stage, generation of a plan; third stage, execution of the plan. For each of the stages fuzzy rules may be used and combined with other techniques used for other stages.

## Slide 17: Optimization and Decision Making
These two generic problems are about finding an optimal option among a set of options. This process is difficult to model when the decision is required to be "humanlike," especially in a group decisionmaking process.

## Slide 18: Optimization
Optimization problems sometimes do not have well-defined parameters and values. Finding an optimal solution in this case is extremely difficult. For example, the cost from one town to another for the TSP case example might not be a single value, but an interval or a fuzzy number, say, about 600. A fuzzy solution to this problem when inexact costs are provided instead of exact values is presented in Dubois and Prade (1988).

## Slide 19: Decision Making
Fuzzy logic, when applied to decision-making problems, provides formal methodology for problem solving, and human consistency. These are important general characteristics of fuzzy decision making systems. Such systems should have the following functionality:
Explain the solution to the user
Keep a rigorous and "fair" way of reasoning;
Accommodate subjective knowledge
Account for "grayness" in the solution process, when, for example, it is impossible to draw a rigid border between "bad" and "good."

## Slide 20: Decision Making
Fuzzy logic can either be used instead of, or in addition to, probability theory. For example, suppose we have the probability distribution for the monthly sales of item x over a certain period of time. The distribution can be used to estimate the probability p(xi) that a certain amount of this item will be sold next month. But to make a decision on what should be produced next month, it is necessary to know whether the predicted through probability p(xi) sell of x is "good" or "bad," or "OK," from the point of view of the profit of the company. So we have to define the fuzzy concepts of "good" and "bad'' for this particular company.

## Slide 21: Decision Making
Solving decision-making problems by using fuzzy systems was illustrated in previous lecture of this course with the Bank Loan case example. Similar decision-making tasks are investment advising, mortgage approval, insurance risk evaluation, house pricing, selecting the best candidate for a job, assessing complex projects, assessing student papers, assessing the risk of failure of a company, and many others.

## Slide 22: Group Decision Making
Fuzzy reasoning particularly suits modeling a group decision-making process. The following terms relate to this task:
A group of individuals (experts): x1, x2, . . .,xp
A set of options: s1, s2, . . .,sn
Parameters describing the experts' opinions and preferences

## Slide 23: Group Decision Making
And the task is to find the option si on which there is a consensus among the experts. Two approaches to using fuzzy logic for this problem are:
Using linguistic quantified propositions of the form of QBx are F. For example, Q denotes "most"; B denotes "important"; x denotes "expert"; F denotes "convinced." Each of the fuzzy terms can be represented by a membership function on the universe X representing the degree to which each expert x ∊ X ''belongs" to the fuzzy set.

## Slide 24: Group Decision Making
  A value μF(xi) denotes how much convinced expert xi is with regard to the option under discussion for consensus. The final truth-value of the proposition "most important experts are convinced" is calculated as:

## Slide 25: Group Decision Making
Using fuzzy preference relations. In this case a fuzzy relation Rk:SxS → [0, 1] represents the preference of the expert xk between each of the pairs (si_sj) of options for decision. One way to process these fuzzy preference relations to achieve the final preference relation R over all the experts before finding the optimal solution from it is given below:

## Slide 26: Group Decision Making
Fuzzy methods for modeling group decision-making is an area of growing interest.

## Slide 27: MATLAB Fuzzy Toolbox

## Slide 28: Introduction
Fuzzy Logic Toolbox™ provides MATLAB® functions, graphical tools, and a Simulink® block for analyzing, designing, and simulating systems based on fuzzy logic. The product guides you through the steps of designing fuzzy inference systems. Functions are provided for many common methods, including fuzzy clustering and adaptive neurofuzzy learning.

## Slide 29: Introduction
The toolbox lets you model complex system behaviors using simple logic rules and then implement these rules in a fuzzy inference system. You can use it as a standalone fuzzy inference engine. Alternatively, you can use fuzzy inference blocks in Simulink and simulate the fuzzy systems within a comprehensive model of the entire dynamic system.

## Slide 30: Working with the Fuzzy Logic Toolbox
The Fuzzy Logic Toolbox provides GUIs to let you perform classical fuzzy system development and pattern recognition. Using the toolbox, you can:
Develop and analyze fuzzy inference systems
Develop adaptive neurofuzzy inference systems
Perform fuzzy clustering
In addition, the toolbox provides a fuzzy controller block that you can use in Simulink to model and simulate a fuzzy logic control system. From Simulink, you can generate C code for use in embedded applications that include fuzzy logic.

## Slide 31: Building a Fuzzy Inference System
Fuzzy inference is a method that interprets the values in the input vector and, based on user-defined rules, assigns values to the output vector. Using the GUI editors and viewers in the Fuzzy Logic Toolbox, you can build the rules set, define the membership functions, and analyze the behavior of a fuzzy inference system (FIS). The following editors and viewers are provided:
FIS Editor - Displays general information about a fuzzy inference system
Membership Function Editor - Lets you display and edit the membership functions associated with the input and output variables of the FIS

## Slide 32: Building a Fuzzy Inference System
Rule Editor - Lets you view and edit fuzzy rules using one of three formats: full English-like syntax, concise symbolic notation, or an indexed notation
Rule Viewer - Lets you view detailed behavior of a FIS to help diagnose the behavior of specific rules or study the effect of changing input variables
Surface Viewer - Generates a 3-D surface from two input variables and the output of an FIS

## Slide 33: Building a Fuzzy Inference System
The Membership Function Editor (top left), FIS Editor (center), Rule Editor (top right), Rule Viewer (bottom left), and Surface Viewer (bottom right).

## Slide 34: Modeling Using Fuzzy Logic
The Fuzzy Logic Toolbox lets you apply neurofuzzy and clustering techniques to model and classify system behavior.
Adaptive Neurofuzzy Inference
  Using the Adaptive Neuro-Fuzzy Inference System (ANFIS) Editor, you can shape membership functions by training them with input/output data rather than specifying them manually. The toolbox uses a back propagation algorithm alone or in combination with a least squares method, enabling your fuzzy systems to learn from the data.

## Slide 35: Modeling Using Fuzzy Logic
The ANFIS Editor constructs and tunes a FIS based on the data being modeled.

## Slide 36: Modeling Using Fuzzy Logic
Fuzzy Clustering
  The Fuzzy Logic Toolbox provides support for fuzzy C-means and subtractive clustering, modeling techniques for data classification and modeling.

## Slide 37: Simulating and Deploying Fuzzy Inference Systems
You can evaluate FIS performance by using the Fuzzy Logic Controller block in a Simulink model of your system. The Fuzzy Logic Controller block automatically generates a hierarchical block diagram representation for most fuzzy inference systems. This representation uses only built-in Simulink blocks, enabling efficient code generation (using Simulink Coder, available separately).
You can also save your FIS in ASCII format for use outside the MATLAB environment. The toolbox supplies a fuzzy inference engine that can execute your fuzzy system as a stand-alone application or embedded in an external application.

## Slide 38: FuzzyCLIPS
Lecture 13

## Slide 39: Introduction
FuzzyCLIPS is a fuzzy logic extension of the CLIPS (C Language Integrated Production System) expert system shell from NASA. It was developed by the Integrated Reasoning Group of the Institute for Information Technology of the National Research Council of Canada and has been widely distributed for a number of years. It enhances CLIPS by providing a fuzzy reasoning capability that is fully integrated with CLIPS facts and inference engine allowing one to represent and manipulate fuzzy facts and rules.

## Slide 40: Introduction
FuzzyCLIPS can deal with exact, fuzzy (or inexact), and combined reasoning, allowing fuzzy and normal terms to be freely mixed in the rules and facts of an expert system. The system uses two basic inexact concepts, fuzziness and uncertainty. It has provided a useful environment for developing fuzzy applications but it does require significant effort to update and maintain as new versions of CLIPS are released.

## Slide 41: Fuzzy Facts in FuzzyCLIPS
Fuzzy facts may be defined, matched as a pattern in a rule, and asserted in a manner similar to the ordinary crisp
facts employed in standard CLIPS.
Example 1
(deftemplate age ;definition of fuzzy variable ‘age’
0 120 years
( (young (25 1) (50 0))
(old (50 0) (65 1))
)
)

## Slide 42: Fuzzy Facts in FuzzyCLIPS
(deffacts fuzzy-fact
(age young) ; a fuzzy fact
)
(defrule one ; a rule that matches and asserts fuzzy facts
(Speed_error big)
=>
(assert (Throttle_change small))
)
where young, big and small are fuzzy terms, and age, Speed_error and Throttle_change are linguistic (fuzzy) variables.

## Slide 43: Fuzzy Facts in FuzzyCLIPS
Each linguistic (fuzzy) variable has an associated fuzzy term set (called primary terms in FuzzyCLIPS) that is the set of values that the fuzzy variable may take. For example, the fuzzy variable water_temperature might have the primary term set {cold, warm, hot}, where each primary term represents a specific fuzzy set

## Slide 44: Fuzzy Facts in FuzzyCLIPS
Primary terms of a linguistic variable

## Slide 45: Uncertainty
Uncertainty occurs when one is not absolutely certain about a piece of information. The degree of uncertainty is usually represented by a crisp numerical value on a scale from 0 to 1, where a certainty factor6 of 1 indicates that the expert system is very certain that a fact is true, and a certainty factor of 0 indicates that it is very uncertain that a fact is true.
In FuzzyCLIPS, a fact is composed of two parts: the fact in the sense of standard CLIPS and its certainty factor.

## Slide 46: Uncertainty
In general a FuzzyCLIPS fact takes the following form:
(fact) [CF certainty factor]
The CF acts as the delimiter between the fact and the certainty factor and [ ] indicates an optional part. For example,
(prediction sunny) CF 0.8
is a fact that indicates that the weather will be sunny with a certainty of 80%. However, if the certainty factor is omitted, as in a normal CLIPS fact,
(prediction sunny)
then FuzzyCLIPS assumes that the weather will be sunny with a certainty of 100%.

## Slide 47: Uncertainty
Certainty factors may also be associated with entire rules, as illustrated by Example 2.
Example 2
(defrule flight-rule
(declare (CF 0.95)) ;declares certainty factor of the rule
(animal type bird)
=>
(assert (animal can fly))
)
represents the hypothesis that, 95% of the time, if an animal is a bird, then it can fly. Similar to facts, if the certainty factor of a rule is not declared, it is assumed to be equal to the value 1.0.

## Slide 48: Uncertainty
Uncertainty and fuzziness can occur simultaneously (see Example 3).
Example 3
(deffacts FuzzyAndUncertainFact
(Speed_error more_or_less zero) CF 0.9
)
(defrule Uncertain_rule
(declare (CF 0.8) )
(Johns_age young)
=>
(assert (John goes to school))
)
where Speed_error and Johns_age are fuzzy variables, zero and young are fuzzy terms, more_or_less is a fuzzy term modifier and 0.9 and 0.8 are certainty factors associated with a fact and a rule respectively.

## Slide 49: Inference Techniques
Rule evaluation depends on a number of different factors, such as whether or not fuzzy variables are found in the antecedent or consequent part of a rule, whether a rule contains multiple antecedents or consequents, whether a fuzzy fact being asserted has the same fuzzy variable as an already existing fuzzy fact (global contribution), and so on.

## Slide 50: Inference Techniques Simple Rules
Consider the simple rule of the form
if A then C CFr
A’ CFf
------------------------
C’ CFc
where:
A is the antecedent of the rule
A’ is the matching fact in the fact database
C is the consequent of the rule
C’ is the actual consequent calculated
CFr is the certainty factor of the rule
CFf is the certainty factor of the fact
CFc is the certainty factor of the conclusion

## Slide 51: Inference Techniques Simple Rules
Three types of simple rules are defined: CRISP_, FUZZY_CRISP, and FUZZY_FUZZY. If the antecedent of the rule does not contain a fuzzy object, then the type of rule is CRISP_ regardless of whether or not a consequent contains a fuzzy fact. If only the antecedent contains a fuzzy fact, then the type of rule is FUZZY_CRISP. If both antecedent and consequent contain fuzzy facts, then the type of rule is FUZZY_FUZZY.

## Slide 52: CRISP_ Simple Rule
If the type of rule is CRISP_, then A’ must be equal to A in order for this rule to fire. This is a “normal” CLIPS rule (actually A would be a pattern and A’ would match the pattern specification, but for simplicity we will not deal with patterns). In that case the conclusion C’ is equal to C, and
CFc = CFr * CFf

## Slide 53: CRISP_ Simple Rule
Given a rule:
(defrule crisp-simple-rule
(declare (CF 0.7)) ;crisp rule certainty factor of 0.7
(light_switch off) ;crisp antecedent
=>
(assert (illumination_level dark)) ; fuzzy consequent
) ; end of rule definition
and given that the fact:
(light_switch off) CF 0.8
has been asserted.
Then the following fact will be asserted into the fact database due to the
firing of the crisp-simple-rule:
(illumination_level dark) CF 0.56
where the certainty factor of the conclusion has been calculated as follows
CFc = 0.7 * 0.8

## Slide 54: FUZZY_CRISP Simple Rule
If the type of rule is FUZZY_CRISP, then A’ must be a fuzzy fact with the same fuzzy variable as specified in A for a match to occur and the rule to be placed on the agenda. In addition, while values of the fuzzy variables A and A’ represented by the fuzzy sets Fa and F’a do not have to be equal, they must overlap.
For example, the fuzzy facts (temperature high) and (pressure high) do not match because the fuzzy variables temperature and pressure are not the same.

## Slide 55: FUZZY_CRISP Simple Rule
Matching of fuzzy facts: clearly (pressure low) and (pressure medium) overlap and thus match, while (pressure low) and (pressure high) do not match

## Slide 56: FUZZY_CRISP Simple Rule
For a FUZZY_CRISP rule, the conclusion C’ is equal to C, and
CFc = CFr * CFf * S
where S is a measure of similarity between the fuzzy sets Fα (determined by the fuzzy pattern A) and F’α (of the matching fact A’). The measure of similarity is based upon the measure of possibility P and the measure of necessity N. It is calculated according to the following formula
otherwise
where
and
is the complement of Fα described by the following membership function

## Slide 57: FUZZY_CRISP Simple Rule
Therefore, if the similarity between the fuzzy sets associated with the fuzzy pattern (A) and the matching fact (A’) is high the certainty factor of the conclusion is very close to CFr * CFf since S will be close to 1.
If the fuzzy sets are identical then S will be 1 and the certainty factor of the conclusion will equal CFr * CFf. If the match is poor then this is reflected in a lower certainty factor for the conclusion. Note also that if the fuzzy sets do not overlap then the similarity measure would be zero and the certainty factor of the conclusion would be zero as well. In this case the conclusion should not be asserted and the match would be considered to have failed and the rule would not be placed on the agenda.

## Slide 58: FUZZY_CRISP Simple Rule
Example
(defrule simple-fuzzy-crisp-rule
(declare (CF 0.7)) ;rule has a certainty factor of 0.7
(fuzzy-fact fact2) ;fuzzy antecedent
=>
(assert (crisp-fact fact3)) ;crisp consequent
)
where (fuzzy-fact fact1) CF 0.8 is the matching fact in the fact database

## Slide 59: FUZZY_CRISP Simple Rule
We have P = 0.6667 into database
First, the necessity is calculated as N = 1 – P = 0.3333
Since the necessity is less than 0.5, S = (N(Fa | Fa¢) + 0.5) * P(Fa | Fa¢)= = (0.3333 + 0.5) * 0.8 = 0.6667
And thus CFc = (0.7) * (0.8) * (0.6667) = 0.3733.

## Slide 60: FUZZY_FUZZY Simple Rule
If the type of rule is FUZZY_FUZZY, and the fuzzy fact and antecedent fuzzy pattern match in the same manner as discussed for a FUZZY_CRISP rule, then it is shown that the antecedent and consequent of such a rule are connected by the fuzzy relation
R = Fa * Fc
where
Fa is a fuzzy set denoting the value of the fuzzy antecedent pattern
Fc is a fuzzy set denoting the value of the fuzzy consequent

## Slide 61: FUZZY_FUZZY Simple Rule
In the current version of the system (6.10d) the membership function of the relation R is calculated according to the formula
The calculation of the conclusion is based upon the
compositional rule of inference, which can be described as follows:
F’c = F’α ¤ R
where F’c is a fuzzy set denoting the value of the fuzzy object of the consequent.

## Slide 62: FUZZY_FUZZY Simple Rule
The membership function of F’c is calculated as follows
which may be simplified to
where
The certainty factor of the conclusion is calculated according to
CFc = CFr * CFf.

## Slide 63: FUZZY_FUZZY Simple Rule
Example 6
(defrule fuzzy-fuzzy-rule
;both antecedent and consequent are fuzzy objects
(temperature hot)
=>
(assert (temp_change little))
)
(temperature warm) ; a fact in the fact database

## Slide 64: Complex Rules Multiple Consequents
In CLIPS, the consequent part of the rule can only contain multiple patterns (C1, C2 ,..., Cn) with the implicit and
conjunction between them. They are treated as multiple rules with a single consequent. So the following rule:
if Antecedents then C1 and C2 and ... and Cn
is equivalent to the following rules:
if Antecedents then C1
if Antecedents then C2
...
if Antecedents then Cn

## Slide 65: Multiple Antecedents
From the above, clearly, only the problem of multiple patterns in the antecedent with a single assertion in the consequent needs to be considered. If the consequent assertion is not a fuzzy fact, no special treatment is needed since the conclusion will be the crisp (non-fuzzy) fact. However, if the consequent assertion is a fuzzy fact, the fuzzy value is calculated using the following basic algorithm.
If logical and is used, one has
  if A1 and A2 then C CFr
  A’1 CFf1
  A’2 CFf2
  -------------------------------------
  C’ CFc
where A’1 and A’2 are facts (crisp or fuzzy) that match the antecedents A1 and A2 respectively.

## Slide 66: Multiple Antecedents
In this case the fuzzy set describing the value of the fuzzy assertion in the conclusion is calculated according to the formula
F’c = F’c1 ⋂ F’c2
where
⋂ denotes the intersection of two fuzzy sets
F’c1 is the result of fuzzy inference for the fact A’1 and the simple rule if A1 then C
F’c2 is the result of fuzzy inference for the fact A’2 and the simple rule if A2 then C

## Slide 67: Multiple Antecedents
Note that if both A1 and A2 were crisp (non-fuzzy) facts then the conclusion would just be the fuzzy fact C since we would be dealing with two CRISP_FUZZY simple rules.
If one of the patterns is crisp (say A1) and the other is fuzzy then the conclusion is F’c2 since the CRISP_FUZZY simple rule would conclude C and the FUZZY_FUZZY simple rule would conclude F’c2.
The intersection of these two would just be F’c2.

## Slide 68: Multiple Antecedents
The certainty factor of the conclusion is calculated according to MYCIN’s model
CFc = min(CF’f1 ,CF’f2 ) * CFr
where min denotes the minimum of the two numbers and
  CF’f1 is the CF of the simple rule if A1 then C given the matching fact A’1
  CF’f2 is the CF of the simple rule if A2 then C given the matching fact A’2
The above algorithm can be applied repeatedly to handle any combination of antecedent patterns, i.e.,
F’c = F’c1 ⋂ F’c2 ... ⋂ F’cn
CFc = min(CF’f1 , CF’f2, ... , CF’fn) * CFr

## Slide 69: Threshold Certainty Factors
In FuzzyCLIPS it is possible to set a threshold certainty factor value such that no rule will be fired unless the rule has a calculated certainty factor value greater than or equal to the threshold value. This feature may be useful in preventing a chain of rules with very low certainty and little logical contribution from firing, and thus speed up the run time. The default is to have no threshold certainty factor set (i.e., a threshold of 0.0), and for rules to be fired as usual. The calculated certainty factor for a rule is
CFrule * min(CF1, ... ,CFn)
where CFrule is the certainty factor for the rule and CFi are the certainty factors for the facts that matched the n patterns on the lefthand side of the rule.

## Slide 70: Threshold Certainty Factors
Example 7
(defrule below-threshold-rule
(declare (CF 0.5)) ;rule certainty factor of 0.5
(fuzzy-fact antecedent-fact) ;fuzzy antecedent
=>
(assert (crisp-fact c1)) ;crisp consequent
(assert (another-fuzzy-fact c2)) ;fuzzy consequent
)
Suppose the following fact has been asserted
(fuzzy-fact fact-list-fact) CF 0.6
The calculated certainty factor for the rule is
CF = 0.5 * 0.6 = 0.3

## Slide 71: Threshold Certainty Factors
The rule will fire only if the threshold certainty factor is less than or equal to 0.3 at the time the rule is selected to fire.
The certainty factor for (another-fuzzy-fact c2), the fuzzy consequent in the previous rule, is
CF = 0.5 * 0.6 = 0.3
from equation for a simple FUZZY_FUZZY rule. However, the certainty factor for (crisp-fact c1) is
CF = 0.5 * 0.6 * S,
where S is the measure of similarity, as for a simple FUZZY_CRISP rule.

## Slide 72: Threshold Certainty Factors
Suppose that S=0.8. Then the following conclusions are reached on the RHS
=>
(assert (crisp-fact c1)) ;calculated CF = 0.24
(assert (another-fuzzy-fact c2)) ;calculated CF = 0.3
Combining rule certainty factors, fact certainty factors, multiple patterns on the lefthand side of a rule and multiple assertions on the righthand side of a rule can lead to a complicated determination of threshold and certainty factors for the asserted facts.

## Slide 73: Threshold Certainty Factors
Example 8
(defrule complex
(declare (CF 0.9))
(crisp1)
(fuzzy1 very few)
=>
(assert (crisp2)
(fuzzy2 hot))
)
with asserted facts
(crisp1) CF 0.8
(fuzzy1 few) CF 0.7
The calculated certainty factor for the rule is
0.9 * min(0.8, 0.7) = 0.63

## Slide 74: Threshold Certainty Factors
Therefore the rule will fire if the threshold value is less than or equal to 0.63 and the certainty factors of the two asserted facts will be (assuming the similarity between (fuzzy1 very few) and (fuzzy1 few) is 0.6)
CF of (crisp2) = 0.9 * min(0.8, 0.7*0.6) = 0.378
CF of (fuzzy1 few) = 0.9 * min(0.8, 0.7) = 0.63

## Slide 75: Certainty Factors in Assert Statements
When a fact is asserted in FuzzyCLIPS, its certainty factor may be specified. It is thus possible to assert a fact on the RHS of a rule with a specific certainty factor.
Example 9
(assert (some-consequent) CF 0.8) ;asserting fact with CF = 0.8
Note that a certainty factor will also be calculated according to the nature of the rule (having multiple antecedents, FUZZY_FUZZY, CRISP_, or FUZZY_CRISP) and any global contribution. This calculated certainty factor will then be multiplied by the certainty factor given in the assert statement. This could be useful as a method of assigning weighted certainty factors for a rule with multiple consequents.

## Slide 76: Certainty Factors in Assert Statements
Example 10
(defrule assert-cf-rule
(declare (CF 0.8));rule CF is 0.8
(fact 1)
=>
(assert (c1))
(assert (c2) CF 0.7) ;assert c2 with CF 0.7
(assert (c3))
(assert (c4))
)

## Slide 77: Certainty Factors in Assert Statements
where
(fact 1) CF 0.9 ; matching fact has CF 0.9
the conclusions reached on the RHS would be:
  (assert (c1)) ; CF = 0.8*0.9 = 0.72
  (assert (c2) CF 0.7) ; CF = 0.8*0.9*0.7 = 0.504
  (assert (c3)) ; CF = 0.8*0.9 = 0.72
  (assert (c4)) ; CF = 0.8*0.9 = 0.72
The above rule attaches a lower CF to conclusion c2 than to the other conclusions.

## Slide 78: Defuzzification
A method which has been widely adopted is to take the center of gravity COG or moment) of the whole set. This has the advantage of producing smoothly varying controller output, but it is sometimes criticized as giving insufficient weight to rule consequents that agree and ought to reinforce each other.
Another method concentrates on the values where the possibility distribution reaches a maximum, called the mean of maxima method. The mean of maxima (MOM) algorithm is criticized as producing less smooth controller output, but has the advantage of greater speed due to fewer floating-point calculations.
In FuzzyCLIPS, the user has the option of choosing either the COG or MOM algorithm when defuzzifying a fuzzy set

## Slide 79: Centre of Gravity Algorithm
In FuzzyCLIPS, a fuzzy set is defined by a set of points that are considered to be connected by straight-line segments.
where xi´ is the local centre of gravity, Ai is the local area of the shape underneath line segment (pi-1, pi), and n is the total number of points.

## Slide 80: Mean of Maxima Algorithm
The MOM algorithm returns the x-coordinate (x”) of the point at which the maximum membership (y) value of the set is reached.
If the maximum y value is reached at more than one point, then the average of all the x” is taken. More formally:
where x”j are the x-coordinates of all the maxima, and J is the total number of maxima .

## Slide 81: Defuzzification
(moment-defuzzify ?<fact-var> | integer | <fuzzy-value>) ; COG algorithm
(maximum-defuzzify ?<fact-var> | integer | <fuzzy-value>) ; MOM algorithm
The argument may be fact variable (?<fact-var>), which normally is bound on the LHS of a rule . It may be the integer value of a fact number (i.e., the index of the fact on the fact list). It may also be a <fuzzy-value > that can be obtained (among other ways) by matching in the pattern of a fuzzy deftemplate fact or a FUZZY-VALUE slot.

## Slide 82: Defuzzification
Example 33
Suppose that fact-1 (a fuzzy deftemplate fact) on the fact list is (temperature warm) and that the COG method returns a value of 28, while the MOM method returns a value of 32.5.
When the following defuzzification command is issued at the CLIPS prompt level it will return the value 28.0 and display this value at the CLIPS prompt level
(moment-defuzzify 1)
When either of the following rules are executed it will print ‘Temperature is 32.5’.

## Slide 83: Defuzzification
Example 33
(defrule defuzzification-1
  ?f <- (temperature ?) ; ? used to assure match of the
  ; temperature fuzzy fact
  =>
  (bind ?t (maximum-defuzzify ?f)) ; get the value
  (printout t “Temperature is “ ?t crlf) ; print 32.5
)
(defrule defuzzification-2
  (temperature ?fv) ; ?fv used to hold the fuzzy value
  ; of the matching fuzzy fact
  =>
  (printout t “Temperature is “ (maximum-defuzzify ?fv) crlf)
)

## Slide 84: Using the FuzzyCLIPS Extensions
Lecture 14

## Slide 85: Defining Fuzzy Variables in Deftemplate Constructs
All fuzzy variables must be predefined before use with the deftemplate statement. This is an extension of the standard deftemplate construct in CLIPS. The extended syntax of this construct is as follows:
(deftemplate <name> [“<comments>”]
<from> <to> [<unit>] ; universe of discourse
(
  t1
  .
  . ; list of primary terms
  .
  tn
)
)

## Slide 86: Defining Fuzzy Variables in Deftemplate Constructs
<name> is the identifier used for the fuzzy variable. The description of the universe of discourse consists of three elements.
The <from> and <to> should be floating point numbers. They represent the beginning and end of the interval that describes the domain of the fuzzy variable (the universe of discourse). The value of <from> must be less than the value for <to>.
The <unit> is a word that represents the unit of measurement (optional).
The ti are specifications for the fuzzy terms (such as hot, cold, warm) used to describe the fuzzy variable. These specifications describe the shape of the fuzzy set associated with the terms.

## Slide 87: Primary Terms
A primary term ti (i=1, ..., n) has the form
(<name> <description of fuzzy set>)
where <name> represents the name of a primary term used to describe a fuzzy concept, and
<description of fuzzy set> defines a membership function of the given primary term.
The membership function can be described using either a singleton representation, a standard function representation, or a linguistic expression that uses terms defined previously in the fuzzy deftemplate definition.
<description of fuzzy set> ::= <singletons> | <standard> | <linguistic-expr>

## Slide 88: Singleton Representation
The grade of membership μA(x) of x in fuzzy set A is a positive number and the pair (μA(x), x) will be called a singleton (often these pairs are represented by μA(x)/x or μ(x)/x for short). A fuzzy set A in a universe of discourse U can be described as follows:
where the integration symbol denotes the union of singletons.

## Slide 89: Singleton Representation
If a universe of discourse U is a finite set, then A is expressed as follows:
In FuzzyCLIPS we consider the universe of discourse to be a range of the real number line and do not deal with finite sets for U. A singleton will be represented here as a pair (xi m(xi )) . A fuzzy set A will be represented as a list of singletons
<singletons> ::= (x1 μ1) (x2 μ2) . . . (xn μn)
where:
xi ≤ xi+1 for i = 1, 2, ... , n-1
xi is an element from U
μi is a number denoting the grade of membership of x in the fuzzy set A

## Slide 90: Singleton Representation
A fuzzy set is represented by an ordered set of points joined by straight line segments.
The grade of membership of an x value not listed in a list of singletons will be calculated on the basis of interpolation according to the following formula:

## Slide 91: Singleton Representation
Example 14
Let U = {x | 0 £ x £ 9}
We may then define a fuzzy set “few” as follows
m(0) = 0, m(1) = 0, m(2) = 0.3, m(3) = 0.9,
m(4) = 1, m(5) = 0.8, m(6) = 0.5, m(7) = 0,
m(8) = 0, m(9) = 0
One can represent this fuzzy set by the following list of singletons
(1 0) (2 0.3) (3 0.9) (4 1) (5 0.8) (6 0.5) (7 0)

## Slide 92: Singleton Representation
One can also show this set graphically as in Figure below: Fuzzy Set of group few.

## Slide 93: Singleton Representation
In FuzzyCLIPS one can define a linguistic variable group that has a universe of discourse from 0 to 9 (units unspecified) and the primary term few as follows:
(deftemplate group ;a linguistic variable declaration
0 9 ;universe of discourse limits (no units)
( ;start of primary term declarations
  ; a primary term few described in singleton notation
(few (1 0) (2 0.3) (3 0.9) (4 1) (5 0.8) (6 0.5) (7 0))
) ;end of primary term declarations
) ;end of fuzzy deftemplate

## Slide 94: Singleton Representation
Note that it is possible for consecutive x values to be the same. This describes a crisp boundary in the fuzzy set (vertical line). If more than three points have the same value then only three will be kept (the fourth will always replace the third). If two points have exactly the same x and y values then one of them will be discarded. Consider the following two examples of fuzzy sets with crisp boundaries.
Example 15
The singleton set described as
(three (3 0) (3 1) (3 0))
might represent the crisp concept 3 as a fuzzy set.

## Slide 95: Singleton Representation
Example 16
Another more complex (and probably unrealistic) set might be defined with the following set of singleton values
  (weird (1 0) (1 1) (1 0) (3 0) (4 .25)
  (4 1) (4 .4) (4 .5) (6 1) (8 0) )
Note that in this case the point (4 .4) is discarded.

## Slide 96: Standard Function Representation
Frequently, it is useful to describe a membership function using one of a set of standard functions S, P, or Z.
Parameters of these functions can be chosen, depending on applications. These functions are defined as follows and are shown graphically in next slides.

## Slide 97: Standard Function Representation
S function

## Slide 98: Standard Function Representation
Z function

## Slide 99: Standard Function Representation
∏ function

## Slide 100: Standard Function Representation
A standard representation of a membership function has the following format:
<standard> ::= (S a c) | (s a c) | (Z a c) | (z a c) | (PI d b) | (pi d b)
where : a, b, c, d are numbers that represent the parameters of the respective functions.
Example 17
(deftemplate Tx “output water temperature”
5 65 Celsius
( (cold (z 10 26)) ;standard set representation
(OK (PI 2 36))
(hot (s 37 60))
)
)

## Slide 101: Standard Function Representation
As a special note, consider the case where the parameter a is equal to c for the S or Z functions. In this case two points will be used to represent the function.
Example 18
(S 10 10) will be represented (10 0) (10 1)
(Z 10 10) will be represented (10 1) (10 0)
For the PI function, if parameter d is zero then the function will be represented by three points.
Example 19
(PI 0 10) will be represented (10 0) (10 1) (10 0)

## Slide 102: Linguistic Expression Representation
Example 20
(deftemplate temperature
  0 100 C
  ( (cold (z 10 26)) ;standard set representation
  (hot (s 37 60)) ;standard set representation
  (warm not [ hot or cold ]) ; linguistic expression
  )
)
Note that the term warm is described as being not hot or cold. It uses the terms hot and cold previously defined in this deftemplate to describe the warm concept. Only terms described in this deftemplate (before the term definition being defined) can be used (along with any available modifiers and the and and or operations).

## Slide 103: Standard Deftemplate Definitions with Fuzzy Slots (fields)
A fuzzy deftemplate describes a fuzzy variable. One may use these deftemplates to describe fuzzy facts in patterns and assert commands. For example,
(defrule high-temp
  (temperature hot)
  =>
  (assert (move-throttle negative-big)
  (printout t “The temperature is hot”)
)
contains a fuzzy pattern based on the fuzzy deftemplate temperature. It also contains an assertion of a fuzzy fact based on the fuzzy deftemplate for move-throttle. Facts that have as their relation name the name of a fuzzy deftemplate will be referred to as fuzzy deftemplate facts.

## Slide 104: Standard Deftemplate Definitions with Fuzzy Slots (fields)
These facts in essence have a single slot that holds the fuzzy value described by the linguistic expression (or fuzzy set description). It is also possible to supplement standard CLIPS deftemplate facts by having one or more of the slots be a fuzzy value slot. In these cases the slot is associated with a fuzzy deftemplate description so that the appropriate universe of discourse and terms are known.
These facts with fuzzy slots are known as fuzzy facts.14 A fuzzy slot has the form
(fuzzy-slot> ::= (slot <slotname> (type FUZZY-VALUE <fuzzy-deftemplate-name>)
where <slotname> is the name of the slot and <fuzzy-deftemplate-name> is the name of a previously defined fuzzy deftemplate.

## Slide 105: Standard Deftemplate Definitions with Fuzzy Slots (fields)
Example 21
;; assume that the fuzzy deftemplates fz-height and
;; fz-weight have already been defined
(deftemplate person
  (slot name (type SYMBOL))
  (slot height (type FUZZY-VALUE fz-height))
  (slot weight (type FUZZY-VALUE fz-weight))
)
(defrule big-person
  (person (name ?n)
  (weight heavy)
  (height tall))
  =>
  (printout t ?n “ is a big person” crlf)
)

## Slide 106: Modifiers (Hedges) and Linguistic Expressions
Modifiers (very, slightly, etc.) used in phrases such as
very hot or slightly cold
change (modify) the shape of a fuzzy set in a way that suits the meaning of the word used. These modifiers are commonly referred to as hedges. FuzzyCLIPS has a set of predefined modifiers that can be used at any time to describe fuzzy concepts when fuzzy terms are described in fuzzy deftemplates, fuzzy rule patterns are written, or fuzzy facts or fuzzy slots are asserted.

## Slide 107: Modifiers (Hedges) and Linguistic Expressions
Modifier Name | Modifier Description
Not | 1-y
Very | y**2
Somewhat | y**0.3333
More or less | y**0.5
Extremely | y**3
Intensify2 | y**2 if y in [0,0.5] 1-2*(1-y)**2 if y in (0.5,1]
Plus | y**1.25
Norm | normalizes the fuzzy set so that the maximum value of the set is scaled to be 1.0 ( y = y*1.0/max-value )
Slightly | intensify ( norm (plus A AND not very A))

## Slide 108: Modifiers (Hedges) and Linguistic Expressions
These modifiers change the shape of a fuzzy set using mathematical operations on each point of the set. In the above table the variable y represents each membership value in the fuzzy set and A represents the entire fuzzy set (i.e., y**2 squares each membership value and very A applies the very modifier to the entire set).
Note that when a modifier is used it can be used in upper or lower case (NOT or not) or even a mix of cases (NoT).

## Slide 109: Modifiers (Hedges) and Linguistic Expressions
These predefined modifiers are available for use at all times in fuzzy deftemplate definitions, fuzzy patterns specifications, fuzzy slot assert specifications, and in the fuzzy-modify function. Some examples below illustrate the use of the modifiers.
Example 22
(deftemplate temp
  0 100 C
  ( (cold (Z 20 40))
  (hot (S 60 80))
  (freezing extremely cold)
  )
)
(defrule temp-rule
  (temp not hot and not cold)
  =>
  (printout t “It’s such a pleasant day” crlf)
)

## Slide 110: User Defined Modifiers
The FuzzyCLIPS user may also define modifiers that can be used in exactly the same manner as the predefined ones. This can be done at the FuzzyCLIPS code level or for more complicated definitions or for efficiency at the “C” code level.
Adding a new modifier at the FuzzyCLIPS level is done with the function

## Slide 111: User Defined Modifiers
(add-fuzzy-modifier modname modfunction)
where
modname is the name (symbol) to be used for the modifier and
modfunction is the name of a CLIPS function or a user defined deffunction that takes a floating point number and returns a floating point number (the function should return a number between 0 and 1 and if it does not then it will be set to 0 if it is less than 0 or to 1 if it is greater than 1; the function will be passed numbers between 0 and 1)

## Slide 112: User Defined Modifiers
Example 23
(add-fuzzy-modifier my-somewhat sqrt)
  (deffunction most-extremely-fcn (?x)
  (** ?x 5)
)
(add-fuzzy-modifier most-extremely most-extremely-fcn)
  (deftemplate temp
  0 100 C
  ( (low (10 1) (50 0))
  (high (50 0) (90 1))
  (sort-of-high my-somewhat high)
  (incredibly-low most-extremely low)
)
)

## Slide 113: User Defined Modifiers
In Example 23 sqrt is a system defined function that returns the square root of a number. With this definition the modifier my-somewhat will act exactly like the somewhat modifier supplied with the system. The function mostextremely-fcn is a user defined deffunction that will handle the work of the modifier most-extremely. With this definition its behavior will be similar to that of the system supplied modifier extremely. The functionality of the modifiers defined this way is somewhat limited (for example, it would not be possible to define the above, below, or slightly modifiers this way).
It is also possible to remove any modifiers added this way with the function
(remove-fuzzy-modifier modname)
Note that only modifiers added with the add-fuzzy-modifier function can be removed.

## Slide 114: Linguistic Expressions
The use of fuzzy primary terms and modifiers together with the binary operators and and or allow us to express the problem solutions in a more natural way. These expressions are called linguistic expressions. Expressions such as
  temperature very hot or very cold
  height below tall and above short
are examples of expressions that could be used to describe fuzzy variable. The BNF that describes formally the syntax of such expressions is shown below.

## Slide 115: Linguistic Expressions
<LExpr> ::= <LTerm> | <LExpr> OR <LTerm>
<LTerm> ::= <modExpr> | <LTerm> AND <modExpr>
<modExpr> ::= MODIFIER <modExpr> | <element>
<element> ::= PRIMARY-TERM | [ <LExpr> ]
where
MODIFIER is a valid modifier (not, very, etc.)
PRIMARY-TERM is a term defined in a fuzzy deftemplate

## Slide 116: Linguistic Expressions
  Note that this gives AND higher precedence than OR and that modifiers are basically unary operators with the highest precedence. One can control the order of the expression evaluation through the use of brackets [ and ]. These brackets must be separated from other items by a space due to the nature of the CLIPS token parser.
  Therefore,
  A or B and C or D
  is the same as
  A or [ B and C ] or D

## Slide 117: Using Fuzzy Variables in LHS Patterns
A fuzzy LHS pattern is of the form
( fuzzy-variable-name <linguistic-expr>)
or
( fuzzy-variable-name ?)
or
( fuzzy-variable-name ?<var-name>)
or
( fuzzy-variable-name ?<var-name> & <linguistic-expr>)
or
(template-name <slot-description>+)

## Slide 118: Using Fuzzy Variables in LHS Patterns
where
+ indicates that there are one or more of the <slot-description> entries, at least one of these is a <fuzzy-slot-description>, and a <fuzzy-slot-description> is
( fuzzy-slot-name <linguistic-expr>)
or
( fuzzy-slot-name ?)
or
( fuzzy-slot-name ?<var-name>)
or
( fuzzy-slot-name ?<var-name> & <linguistic-expr>)

## Slide 119: Using Fuzzy Variables in LHS Patterns
Example 24
(deftemplate group ;declaration of fuzzy variable group
  0 20 members
  ((few (3 1) (6 0)) ;primary term few
  (many (4 0) (6 1)) ;primary term many
  )
)
(defrule simple-LHS
  (group few) ;a simple fuzzy LHS pattern
  ...
)

## Slide 120: Using Fuzzy Variables in LHS Patterns
Example 25
(defrule more-complex-lhs
  ?f <- (group very few or very many)
  =>
  (printout t “We are at the extreme limits of the number of”
  (get-u-units ?f) “ in our club” crlf)
)

## Slide 121: Using Fuzzy Variables in LHS Patterns
Example 26
(deftemplate height
  0 8 feet
  ((short (Z 3 4.5))
  (medium (pi 0.8 5))
  (tall (S 5.5 6))
  )
)
(deftemplate person
  (slot name)
  (slot ht (type FUZZY-VALUE height))
)
(defrule quite-complex-lhs
  (person (name ?n) (ht ?h & very tall))
  =>
  (printout t ?n “ is very tall, with a height of about “
  (maximum-defuzzify ?h) “ “
  (get-u-units ?h) crlf )
)

## Slide 122: Using Fuzzy Variables in Deffacts Constructs
The syntax of the deffacts construct has been extended to allow fuzzy facts to be declared. Both fuzzy and non-fuzzy (crisp) facts can be declared in the same deffacts construct. Also certainty factors for crisp or fuzzy facts may be specified. Fuzzy fact specifications in a deffacts construct have the following form:
(deffacts <deffacts-name> [<comment>]
<RHS-pattern>*
)

## Slide 123: Using Fuzzy Variables in Deffacts Constructs
where <RHS-pattern> has been extended as follows:
<RHS-pattern> ::= <ordered-RHS-pattern> |
<template-RHS-pattern> |
<fuzzy-template-RHS-pattern>
<ordered-RHS-pattern> ::= (<symbol> <RHS-field>+)
[CF <certainty factor> | <certainty factor expression>]
<template-RHS-pattern> ::= (deftemplate-name> <RHS-slot>*)
[CF <certainty factor> | <certainty factor expression>]
<fuzzy-template-RHS-pattern> ::=
(<fuzzy-template-name> <description of fuzzy set>
[CF <certainty factor> | <certainty factor expression>]

## Slide 124: Using Fuzzy Variables in Deffacts Constructs
Example 27
(deffacts groupA “some fuzzy facts”
  (my_group (1 0) (5 1) (7 0)) ;singleton description
  (your_group (z 4 8)) ;standard description
  (their_group (s (+ 1 1) 4))
  (person (name ralph) (ht tall))
)
(deffacts groupB “some fuzzy facts with certainty factors”
  (this_group (1 0) (5 1) (7 0)) CF 0.35
  (that_group (pi 2 (+ 3 4))) CF (+ .2 .3)
)

## Slide 125: Using Fuzzy Variables in Assert Statements
The syntax of the assert construct has been expanded to allow fuzzy facts as arguments, and for the certainty factor of a crisp or fuzzy fact to be specified. The assert command (with a single fact asserted in an assert function call) is of the form
(assert
(<crisp fact> | fuzzy-variable-name <description of fuzzy set> |
template-name <slot-description>+)
[CF <certainty factor> | <certainty factor expression>]
)

## Slide 126: Using Fuzzy Variables in Assert Statements
where
+ indicates that there are one or more of the <slot-description> entries, at least one of these is a <fuzzy-slot-description>, and a <fuzzy-slot-description> is
( fuzzy-slot-name <description of fuzzy set>)
<description of fuzzy set> is
<linguistic-expr> | <standard> | <singletons>
and the certainty factor is optional (if not specified a CF of 1.0 is assumed).

## Slide 127: Using Fuzzy Variables in Assert Statements
Example 28
(assert (group few))
(assert (group (1 0) (5 1) (7 0)) )
(assert (group NOT [ very few OR many ] ))
(assert (group (z 4 8)) )
(assert (person (name john) (ht extremely tall)))
(assert (person (name dan) (ht (pi 0 5.6)))
(assert (temp (24 0) (25 1) (26 0)))

## Slide 128: Using Fuzzy Variables in Assert Statements
Example 29
(defrule assert-rule-1
  (zmin ?minval) ;variable ?minval must be numeric
  (zmax ?maxval) ;variable ?maxval must be numeric
  =>
  (assert
  (group (z ?minval ?maxval))
  ) ;fuzzy set description with variables
)
(defrule assert-rule-2 ;asserts standard set with functions
  (zmin ?minval)
  (zmax ?maxval)
  =>
  (assert (group (z ?minval (+ ?maxval 2))))
)

## Slide 129: Using Fuzzy Variables in Assert Statements
(defrule assert-rule-3 ;asserts singleton set with functions
  (x1 ?x1val)
  (x2 ?x2val)
  =>
  (assert
  (group (?x1val 0) (?x2val 1) ((+ ?x2val 1) 0.6)
  ((sqr ?x2val) 0))
  )
)

## Slide 130: Using Fuzzy Variables in Assert Statements
The assert-string function of CLIPS may also be used to assert fuzzy facts.
Example 30
(assert-string “(group (z 4 8))”)
(assert-string “(group (s 4 (+ 5 3)))“)
(assert-string “(person (name bob) (ht medium))”)

## Slide 131: Using Fuzzy Variables in Assert Statements
The <certainty factor> is a constant numeric value from 0.0 to 1.0.
Example 31
(assert (somefact) CF 0.8) ;with CF of 0.8
(assert (group few) CF (+ 0.2 0.4));with CF of 0.6
A <certainty factor expression> has the same syntax as a <certainty factor>, except that the constant numeric value may be replaced by a variable or function which returns a numeric value between 0.0 and 1.0.

## Slide 132: Using Fuzzy Variables in Assert Statements
Example 32
( defrule assert-rule-4 ;illustrates various CF assertions
  (certainty-factor ?cf) ;where ?cf is between 0 and 1
  ?f <- (somefact)
  =>
  (assert (fact1) CF ?cf)
  (assert (fact3) CF (* 0.8 ?cf))
  (assert (fact5) CF (get-cf ?f))
)

## Slide 133: Certainty Factors of Rules
This section will discuss the syntax for declaring the certainty factor of rules. The certainty factor of a rule may be declared in a manner similar to declaring the rule salience:
(defrule some-rule
  (declare (CF <certainty factor>))
  ......
  =>
  ......
)
The <certainty factor> is a number in the range 0 to 1.

## Slide 134: Certainty Factors of Rules
Example 34
(deffacts initial-facts
(fact1) CF 0.8 ;fact with crisp CF of 0.8
)
(defrule some-other-rule
(declare (CF 0.7)) ;a rule with CF of 0.7
(fact1)
=>
(printout t “Hello!”)
)