## Slide 1: Critical Systems Specification
Lecture 7

## Slide 2: Objectives
To explain how dependability requirements may be identified by analysing the risks faced by critical systems
To explain how safety requirements are generated from the system risk analysis
To explain the derivation of security requirements
To describe metrics used for reliability specification

## Slide 3: Topics covered
Risk-driven specification
Safety specification
Security specification
Software reliability specification

## Slide 4: Dependability requirements
Functional requirements to define error checking and recovery facilities and protection against system failures.
Non-functional requirements defining the required reliability and availability of the system.
Excluding requirements that define states and conditions that must not arise.

## Slide 5: Risk-driven specification
Critical systems specification should be risk-driven.
This approach has been widely used in safety and security-critical systems.
The aim of the specification process should be to understand the risks (safety, security, etc.) faced by the system and to define requirements that reduce these risks.

## Slide 6: Stages of risk-based analysis
Risk identification
  Identify potential risks that may arise.
Risk analysis and classification
  Assess the seriousness of each risk.
Risk decomposition
  Decompose risks to discover their potential root causes.
Risk reduction assessment
  Define how each risk must be taken into eliminated or reduced when the system is designed.

## Slide 7: Risk-driven specification

## Slide 8: Risk identification
Identify the risks faced by the critical system.
In safety-critical systems, the risks are the hazards that can lead to accidents.
In security-critical systems, the risks are the potential attacks on the system.
In risk identification, you should identify risk classes and position risks in these classes
  Service failure;
  Electrical risks;
  …

## Slide 9: Insulin pump risks
Insulin overdose (service failure).
Insulin underdose (service failure).
Power failure due to exhausted battery (electrical).
Electrical interference with other medical equipment (electrical).
Poor sensor and actuator contact (physical).
Parts of machine break off in body (physical).
Infection caused by introduction of machine (biological).
Allergic reaction to materials or insulin (biological).

## Slide 10: Risk analysis and classification
The process is concerned with understanding the likelihood that a risk will arise and the potential consequences if an accident or incident should occur.
Risks may be categorised as:
  Intolerable. Must never arise or result in an accident
  As low as reasonably practical(ALARP). Must minimise the possibility of risk given cost and schedule constraints
  Acceptable. The consequences of the risk are acceptable and no extra costs should be incurred to reduce hazard probability

## Slide 11: Levels of risk

## Slide 12: Social acceptability of risk
The acceptability of a risk is determined by human, social and political considerations.
In most societies, the boundaries between the regions are pushed upwards with time i.e. society is less willing to accept risk
  For example, the costs of cleaning up pollution may be less than the costs of preventing it but this may not be socially acceptable.
Risk assessment is subjective
  Risks are identified as probable, unlikely, etc. This depends on who is making the assessment.

## Slide 13: Risk assessment
Estimate the risk probability and the risk severity.
It is not normally possible to do this precisely so relative values are used such as ‘unlikely’, ‘rare’, ‘very high’, etc.
The aim must be to exclude risks that are likely to arise or that have high severity.

## Slide 14: Risk assessment - insulin pump

## Slide 15: Risk decomposition
Concerned with discovering the root causes of risks in a particular system.
Techniques have been mostly derived from safety-critical systems and can be
  Inductive, bottom-up techniques. Start with a proposed system failure and assess the hazards that could arise from that failure;
  Deductive, top-down techniques. Start with a hazard and deduce what the causes of this could be.

## Slide 16: Fault-tree analysis
A deductive top-down technique.
Put the risk or hazard at the root of the tree and identify the system states that could lead to that hazard.
Where appropriate, link these with ‘and’ or ‘or’ conditions.
A goal should be to minimise the number of single causes of system failure.

## Slide 17: Insulin pump fault tree

## Slide 18: Risk reduction assessment
The aim of this process is to identify dependability requirements that specify how the risks should be managed and ensure that accidents/incidents do not arise.
Risk reduction strategies
  Risk avoidance;
  Risk detection and removal;
  Damage limitation.

## Slide 19: Strategy use
Normally, in critical systems, a mix of risk reduction strategies are used.
In a chemical plant control system, the system will include sensors to detect and correct excess pressure in the reactor.
However, it will also include an independent protection system that opens a relief valve if dangerously high pressure is detected.

## Slide 20: Insulin pump - software risks
Arithmetic error
  A computation causes the value of a variable to overflow or underflow;
  Maybe include an exception handler for each type of arithmetic error.
Algorithmic error
  Compare dose to be delivered with previous dose or safe maximum doses. Reduce dose if too high.

## Slide 21: Safety requirements - insulin pump

## Slide 22: Safety specification
The safety requirements of a system should be separately specified.
These requirements should be based on an analysis of the possible hazards and risks as previously discussed.
Safety requirements usually apply to the system as a whole rather than to individual sub-systems. In systems engineering terms, the safety of a system is an emergent property.

## Slide 23: IEC 61508
An international standard for safety management that was specifically designed for protection systems - it is not applicable to all safety-critical systems.
Incorporates a model of the safety life cycle and covers all aspects of safety management from scope definition to system decommissioning.

## Slide 24: Control system safety requirements

## Slide 25: The safety life-cycle
©Ian Sommerville 2000 Dependable systems specification Slide 25

## Slide 26: Safety requirements
Functional safety requirements
  These define the safety functions of the protection system i.e. the define how the system should provide protection.
Safety integrity requirements
  These define the reliability and availability of the protection system. They are based on expected usage and are classified using a safety integrity level from 1 to 4.

## Slide 27: Security specification
Has some similarities to safety specification
  Not possible to specify security requirements quantitatively;
  The requirements are often ‘shall not’ rather than ‘shall’ requirements.
Differences
  No well-defined notion of a security life cycle for security management; No standards;
  Generic threats rather than system specific hazards;
  Mature security technology (encryption, etc.). However, there are problems in transferring this into general use;
  The dominance of a single supplier (Microsoft) means that huge numbers of systems may be affected by security failure.

## Slide 28: The security specification process

## Slide 29: Stages in security specification
Asset identification and evaluation
  The assets (data and programs) and their required degree of protection are identified. The degree of required protection depends on the asset value so that a password file (say) is more valuable than a set of public web pages.
Threat analysis and risk assessment
  Possible security threats are identified and the risks associated with each of these threats is estimated.
Threat assignment
  Identified threats are related to the assets so that, for each identified asset, there is a list of associated threats.

## Slide 30: Stages in security specification
Technology analysis
  Available security technologies and their applicability against the identified threats are assessed.
Security requirements specification
  The security requirements are specified. Where appropriate, these will explicitly identified the security technologies that may be used to protect against different threats to the system.

## Slide 31: Types of security requirement
Identification requirements.
Authentication requirements.
Authorisation requirements.
Immunity requirements.
Integrity requirements.
Intrusion detection requirements.
Non-repudiation requirements.
Privacy requirements.
Security auditing requirements.
System maintenance security requirements.

## Slide 32: LIBSYS security requirements

## Slide 33: System reliability specification
Hardware reliability
  What is the probability of a hardware component failing and how long does it take to repair that component?
Software reliability
  How likely is it that a software component will produce an incorrect output. Software failures are different from hardware failures in that software does not wear out. It can continue in operation even after an incorrect result has been produced.
Operator reliability
  How likely is it that the operator of a system will make an error?

## Slide 34: Functional reliability requirements
A predefined range for all values that are input by the operator shall be defined and the system shall check that all operator inputs fall within this predefined range.
The system shall check all disks for bad blocks when it is initialised.
The system must use N-version programming to implement the braking control system.
The system must be implemented in a safe subset of Ada and checked using static analysis.

## Slide 35: Non-functional reliability specification
The required level of system reliability required should be expressed quantitatively.
Reliability is a dynamic system attribute- reliability specifications related to the source code are meaningless.
  No more than N faults/1000 lines;
  This is only useful for a post-delivery process analysis where you are trying to assess how good your development techniques are.
An appropriate reliability metric should be chosen to specify the overall system reliability.

## Slide 36: Reliability metrics
Reliability metrics are units of measurement of system reliability.
System reliability is measured by counting the number of operational failures and, where appropriate, relating these to the demands made on the system and the time that the system has been operational.
A long-term measurement programme is required to assess the reliability of critical systems.

## Slide 37: Reliability metrics

## Slide 38: Probability of failure on demand
This is the probability that the system will fail when a service request is made. Useful when demands for service are intermittent and relatively infrequent.
Appropriate for protection systems where services are demanded occasionally and where there are serious consequence if the service is not delivered.
Relevant for many safety-critical systems with exception management components
  Emergency shutdown system in a chemical plant.

## Slide 39: Rate of fault occurrence (ROCOF)
Reflects the rate of occurrence of failure in the system.
ROCOF of 0.002 means 2 failures are likely in each 1000 operational time units e.g. 2 failures per 1000 hours of operation.
Relevant for operating systems, transaction processing systems where the system has to process a large number of similar requests that are relatively frequent
  Credit card processing system, airline booking system.

## Slide 40: Mean time to failure
Measure of the time between observed failures of the system. Is the reciprocal of ROCOF for stable systems.
MTTF of 500 means that the mean time between failures is 500 time units.
Relevant for systems with long transactions i.e. where system processing takes a long time. MTTF should be longer than transaction length
  Computer-aided design systems where a designer will work on a design for several hours, word processor systems.

## Slide 41: Availability
Measure of the fraction of the time that the system is available for use.
Takes repair and restart time into account
Availability of 0.998 means software is available for 998 out of 1000 time units.
Relevant for non-stop, continuously running systems
  telephone switching systems, railway signalling systems.

## Slide 42: Non-functional requirements spec.
Reliability measurements do NOT take the consequences of failure into account.
Transient faults may have no real consequences but other faults may cause data loss or corruption and loss of system service.
May be necessary to identify different failure classes and use different metrics for each of these. The reliability specification must be structured.

## Slide 43: Failure consequences
When specifying reliability, it is not just the number of system failures that matter but the consequences of these failures.
Failures that have serious consequences are clearly more damaging than those where repair and recovery is straightforward.
In some cases, therefore, different reliability specifications for different types of failure may be defined.

## Slide 44: Failure classification

## Slide 45: Steps to a reliability specification
For each sub-system, analyse the consequences of possible system failures.
From the system failure analysis, partition failures into appropriate classes.
For each failure class identified, set out the reliability using an appropriate metric. Different metrics may be used for different reliability requirements.
Identify functional reliability requirements to reduce the chances of critical failures.

## Slide 46: Bank auto-teller system
Each machine in a network is used 300 times a day
Bank has 1000 machines
Lifetime of software release is 2 years
Each machine handles about 200, 000 transactions
About 300, 000 database transactions in total per day

## Slide 47: Reliability specification for an ATM

## Slide 48: Specification validation
It is impossible to empirically validate very high reliability specifications.
No database corruptions means POFOD of less than 1 in 200 million.
If a transaction takes 1 second, then simulating one day’s transactions takes 3.5 days.
It would take longer than the system’s lifetime to test it for reliability.

## Slide 49: Key points
Risk analysis is the basis for identifying system reliability requirements.
Risk analysis is concerned with assessing the chances of a risk arising and classifying risks according to their seriousness.
Security requirements should identify assets and define how these should be protected.
Reliability requirements may be defined quantitatively.

## Slide 50: Key points
Reliability metrics include POFOD, ROCOF, MTTF and availability.
Non-functional reliability specifications can lead to functional system requirements to reduce failures or deal with their occurrence.